## Slide 1
Digital Design & Computer Architecture
Slide 1 of 12
Design & Simulation of a Digital Error Detection System Using Parity
A comprehensive logic design study on parity generation, transmission error checking, and XOR-based verification using Logisim.
SUBMITTED BY
DEPARTMENT & INSTITUTION
Dept. of Computer Science & Eng. Academic Year 2026
Likhita 2620030468
Dheeraj 2620030472
Rupesh 2620030517
Druveen 2620030528

## Slide 2
Design & Simulation of Error Detection System
Slide 2 of 12
Digital Data Integrity: High-speed data transmission across physical communication channels is highly susceptible to noise, attenuation, and electromagnetic interference.
Parity Error Detection: Parity bit generation is a standard, lightweight method used to identify single-bit flips by maintaining odd or even logic states.
Implementation Objective: Design a robust combinational circuit using cascaded XOR gates to compute parity at transmission and verify consistency at reception.
Logisim Validation: Practical schematic modeling and interactive switch simulation to verify real-time error detection flags.
Abstract & Overview

## Slide 3
Digital Communication Principles
Slide 3 of 12
Communication Noise
During digital transmission, transient pulses or signal crosstalk can alter binary bits (0 to 1 or 1 to 0). Without error detection, corrupt commands or corrupted memory streams degrade system reliability.
Redundant Bit Concept
Error detection appends extra redundant bits to the payload. These extra bits carry zero user data but enable the receiver's combinational logic to validate message authenticity.
Introduction to Error Detection

## Slide 4
Hardware Error Detection Requirements
Slide 4 of 12
The Technical Challenge
As microprocessors push to higher clock frequencies, transmission line noise increases. Software-based error checking introduces unacceptable CPU overhead.
Visual Data Comparison
Manual or delayed software verification causes system latency.
Hardware must evaluate bit integrity in nanoseconds.
Need for a minimal gate-count combinational error detector.
TRANSMITTED PAYLOAD
1 0 1 0 [P=0]
Even Parity: Total 1s = 2 (Even State)
CORRUPTED RECEIVED PAYLOAD
1 1 1 0 [P=0]
Single Bit Flip: Total 1s = 3 (Odd State) → ERROR DETECTED!
Problem Statement & Channel Noise

## Slide 5
Core Project Targets
Slide 5 of 12
Circuit Architecture
Design a 4-bit data stream parity generator and receiver checker circuit using optimized logic gates.
Even / Odd Parity Logic
Formulate and implement Boolean parity logic equations based on XOR/XNOR gate cascade structures.
Single-Bit Detection
Ensure reliable detection of single-bit transmission corruption before data reaches memory buses.
Logisim Simulation
Construct the complete digital system schematic in Logisim software to simulate operational conditions.
Test Vector Analysis
Verify system logic across all $2^n$ binary input combinations to demonstrate total reliability.
Academic Foundation
Establish practical insights into error detection protocols vital for DDCA hardware coursework.
Project Objectives & Scope

## Slide 6
Methodology & Modular Design
Slide 6 of 12
Stage Highlights
The input stream undergoes parity calculation in the generator block before transmission. At the receiving terminal, the 5-bit bundle enters an identical XOR network. Any discrepancy between computed and received parity trips the error output state.
System Methodology & Workflow

## Slide 7
Boolean Logic Operations
Slide 7 of 12
XOR Gate Foundation
The Exclusive-OR (XOR) gate serves as a modulo-2 adder. It produces a HIGH (1) output if and only if the number of HIGH inputs is odd.
Input A | Input B | Output (A ⊕ B) | Parity State
0 | 0 | 0 | Even (0 ones)
0 | 1 | 1 | Odd (1 one)
1 | 0 | 1 | Odd (1 one)
1 | 1 | 0 | Even (2 ones)
Even Parity Bit Equation:
Even Parity: Parity bit $P$ is chosen to make total count of 1s in $(Data + P)$ even.
Odd Parity: Parity bit $P$ is chosen to make total count of 1s in $(Data + P)$ odd.
Working Principle & XOR Logic

## Slide 8
Hardware Schematic Topology
Slide 8 of 12
Logic Subsystems
4-Bit Input Line: Connects data switches ($D_3, D_2, D_1, D_0$) directly to the generator block.
Parity Generator: Cascaded 2-input XOR gates (IC 7486) synthesize parity bit $P$.
Transmission Bus: Transmits 5 parallel lines ($D_3, D_2, D_1, D_0, P$) to the receiver.
Parity Checker: A 5-input XOR tree calculates total modulo-2 parity state $E$.
Error Indicator: Output $E = 0$ keeps LED OFF (Valid Data); $E = 1$ triggers LED ON (Corruption).
Hardware Circuit Architecture

## Slide 9
Logisim Simulation Verification
Slide 9 of 12
Simulation Features
Interactive Pin Switches: Toggle bits dynamically to simulate live data input.
Fault Injection: Noise buttons simulate transmission bit flips along channel wires.
Visual Status Indicators: Probe components display logic levels ($0/1$) at intermediate XOR nodes.
LED Output Probe: Instantly alerts user upon parity mismatch.
Single-Bit Error Detected
Logisim Simulation Environment
LED OFF (0)
No Transmission Errors
LED ON (1)

## Slide 10
Input Data ($D_3 D_2 D_1 D_0$) | Generated Parity ($P$) | Transmitted Packet | Received Packet | Error Output ($E$) | Status
1 0 1 0 | 0 | 1 0 1 0 0 | 1 0 1 0 0 (Unchanged) | 0 | 
1 1 0 0 | 0 | 1 1 0 0 0 | 1 1 0 0 0 (Unchanged) | 0 | 
1 0 1 0 | 0 | 1 0 1 0 0 | 1 0 0 0 0 (Bit Flip) | 1 | 
1 1 1 0 | 1 | 1 1 1 0 1 | 0 1 1 0 1 (MSB Flip) | 1 | 
Experimental Truth Table Verification
Slide 10 of 12
Verification Summary: The Logisim model successfully verified all $2^4 = 16$ test vectors. In all single-bit error scenarios, the receiver output line $E$ switched HIGH instantly, validating the combinational circuit design.
Simulation Results & Verification

## Slide 11
Trade-Offs & Application Domains
Slide 11 of 12
Key Advantages
Limitations
Practical Uses
Minimal hardware complexity (uses standard IC 7486 XOR gates).
Extremely low propagation delay and high processing speed.
Zero computational overhead on system processor.
Detects only single-bit or odd numbers of bit errors.
Cannot locate exact corrupt bit position.
Cannot perform error correction (requires retransmission).
Serial protocols (UART / RS-232 communication).
Computer memory subsystems (Parity RAM / L1 Cache).
Bus transmissions in Embedded Microcontrollers.
Advantages, Limitations & Uses

## Slide 12
DDCA Academic Project Presentation
Slide 12 of 12
Thank You!
Conclusion
Future Enhancements
Parity generation provides a fast, economical solution for single-bit transmission error detection.
Cascaded XOR gate networks implement parity generation and checking with minimal gate count.
Logisim simulation proved $100\%$ detection accuracy for single-bit faults across test vectors.
Hamming Code Integration: Expand to 7-bit Hamming code for single-bit error correction.
Cyclic Redundancy Check (CRC): Implement polynomial division for multi-bit burst error checking.
FPGA / Hardware Prototype: Synthesize the design onto a Xilinx/Intel FPGA board.
Conclusion & Future Scope